## Slide 1: Modelling a Cold Atom using a Driven Gyroscope
Project by Edward Taylor and Charlotte Dodd
22/02/2018

## Slide 2: Aims
Drive a gyroscope using a motor
Produce a torque with electromagnetism causing the gyroscope to process
Measure the angular velocity of the rotation and procession
Analyse the accuracy of the gyroscope as a model for the cold atom with the Bloch sphere model.

## Slide 3: Theory
Bloch sphere
Biot-Savart
Helmholtz coil

## Slide 4: Feasibility studies
Driving the rotor of the gyroscope with a current
With small conducting magnets
Tachometer and motor arrangement

## Slide 5: Programming

## Slide 6: Data manipulation
Data input: 0D020001014DA6560000
Put data in pairs: ['0D', '02', '00', '01', '01', ’4D', 'A6', ’56’, ’00’, '00']
Keep pairs needed: ['02' '01' 'A6' '56' '00']
Converted to decimal (from hex): [02, 01, 166, 86, 0]
Find rpm (without unit): float(k[2]) + 256*float (k[3]) + 65536*float(k[4]) = 221.82
Create rpm + decimal place: readings.append((value/(10**(int(k[0])/2 +1),int(k[1])))
Get rpm with unit: [(221.82, 1),…]  221.82 rpm

## Slide 7: Graphing the data
Finding time when reading taken: [(221.82, 1),…]
  Loop over pairs creating list of times cumulatively adding previous time of measurement
    readings.append((float(60/k[0])))  returns a time  list(accumulate(readings)  summing them up
    E.g readings.append(float(60/221.82))  [0.27, a, b, c]  [0.27, 0.27+a, 0.27+a+b, 0.27+a+b+c, …]
Use an arbitrary fit function: params, pcov = optimize.curve_fit(func, time, velocity)
Plot velocity vs time
Extract fit parameters: standard_deviation = np.sqrt(np.diag(pcov))

## Slide 8: Plans
Currently in workshop having motor fitted
Magnet analysis and attachment
Weeks 9-10 is testing
Finishing and report writing

## Slide 9: Method
Tachometer
…

## Slide 10: So far
Research and design of Faraday Disk
Redesign and proposal
Motor design
Code being written to interpret results from the tachometer
Magnet analysis

## Slide 11: FEMM Analysis

## Slide 12: FEMM Analysis

## Slide 13: FEMM Analysis
Force acting on magnets in model magnetic field: 0.139545±0.000001N
Magnetic field strength: 87±1mT
Magnetic field strength from
Boit-Savart law: 9mT
Magnetic moment of magnets: 20.3±0.2mNmT^-1
Credit: hyperphysics

## Slide 14: Summary

## Slide 15: Bibliography