## Slide 1: Modelling a Cold Atom using a Driven Gyroscope
Project by Edward Taylor and Charlotte Dodd
22/02/2018

## Slide 2: Aims
Drive a gyroscope using a motor
Produce a torque with electromagnetism causing the gyroscope to process
Measure the angular velocity of the rotation and procession
Analyse the accuracy of the gyroscope as a model for the cold atom with the Bloch sphere model.
Measure the strength of an external magnetic field

## Slide 3: Theory – Bloch Sphere as a Cold Atom
A cold atom is a quantum system
It can be represented with the Bloch Sphere model
Gyroscope is a good model of a cold atom
Project suggestion, Birmingham University School of Physics and Astronomy.
Nuclear induction, Bloch and Felix, Oct 1946, Phys. Rev. 70 (7-8): 460–474.
Credit: Wikimedia commons

## Slide 4: Theory – Gyroscopic Motion
Credit: hyperphysics
University Physics with modern physics, Young, Freedman and Ford, pages 328-330.

## Slide 5: Progress
Research and design of Faraday Disk
Feasibility study
Redesign and proposal
Motor design
Writing code
Magnet analysis

## Slide 6: Feasibility studies
Faraday Disk
Faraday disk with small conducting magnets
Tachometer and motor arrangement
Applying a processional torque with magnets

## Slide 7: FEMM Analysis

## Slide 8: FEMM Analysis

## Slide 9: FEMM Analysis
Force acting on magnets in model magnetic field: 0.139545±0.000001N
Magnetic field strength: 87±1mT
Magnetic field strength from Boit-Savart law: 9mT
Magnetic moment of magnets: 20.3±0.2mNmT^-1
Credit: hyperphysics

## Slide 10: Method - Tachometer
Tachometer measures rate of rotation
  Tipp-Ex® point on rim
  One byte of data recorded every rotation
  Byte in the form: 0D020001014DA6560000
Used to measure of disk and procession
graphed and data analysed
Credit: Tachometer instruction manual.

## Slide 11: Programming

## Slide 12: Data manipulation
Data input: 0D020001014DA6560000
Put data in pairs: ['0D', '02', '00', '01', '01', ’4D', 'A6', ’56’, ’00’, '00']
Keep pairs needed: ['02' '01' 'A6' '56' '00']
Converted to decimal (from hex): [02, 01, 166, 86, 0]
Find rpm (without unit): float(k[2]) + 256*float (k[3]) + 65536*float(k[4]) = 221.82
Create rpm + decimal place: readings.append((value/(10**(int(k[0])/2 +1),int(k[1])))
Get rpm with unit: [(221.82, 1),…]  221.82 rpm

## Slide 13: Graphing the data
Finding time when reading taken: [(221.82, 1),…]
  Loop over pairs creating list of times cumulatively adding previous time of measurement
    readings.append((float(60/k[0])))  returns a time  list(accumulate(readings)  summing them up
    E.g readings.append(float(60/221.82))  [0.27, a, b, c]  [0.27, 0.27+a, 0.27+a+b, 0.27+a+b+c, …]
Find fit parameters: params, pcov = optimize.curve_fit(func, time, velocity)
Plot velocity vs time
Error on fit parameters: standard_deviation = np.sqrt(np.diag(pcov))

## Slide 14: Future Developments
Motor currently being fitted in workshop
Magnet analysis and attachment
Weeks 9-10: testing
Finishing and report writing

## Slide 15: Summary
Gyroscope as a model of the cold atom
Design and feasibility
Data capture
Future developments

## Slide 16: Bibliography
Digital photo tachometer, model: RM-1501, instruction manual , 2000, RS Components UK.
A gyroscope as a way of modelling atomic transitions, project suggestion, 2015, Birmingham University School of Physics and Astronomy.
Nuclear induction, Bloch and Felix, Oct 1946, Phys. Rev. 70 (7-8): 460–474.
Modelling the motion of a gyroscope and designing and magnetic propulsion system, George Gibbons, 2017, University of Birmingham, School of Physics and Astronomy.
University Physics with modern physics, 13th international edition, Young, Freedman and Ford, 2016, Pearson, pages 328-330.
Michael Orgill